## Slide 1
Dr. Asif Zaman
Professor, CSE, RU
ICE 3161
COMMUNICATION ENGINEERING

## Slide 2: Digital-to-digital Conversion
The conversion involves three techniques:
  line coding,
  block coding, and
  scrambling.

## Slide 3: Analog-to-digital Conversion
…is to change an analog signal to digital data.
The most common technique to change an analog signal to digital data (digitization) is called pulse code modulation (PCM).
A PCM encoder has three processes,
  The analog signal is sampled.
  The sampled signal is quantized.
  The quantized values are encoded as streams of bits.

## Slide 4
Sampling:
  The analog signal is sampled every Ts sec,
  where Ts is the sample interval or period.
  The inverse of the sampling interval is called the sampling rate or sampling frequency and denoted by fs,
  where fs = 1/ Ts.

## Slide 5
There are three sampling methods—
  ideal,
  natural, and
  flat-top
In ideal sampling, pulses from the analog signal are sampled.
In natural sampling, a high-speed
switch is turned on for only the small period of time when the sampling occurs. The
result is a sequence of samples that retains the shape of the analog signal
sample and hold, however, creates flat-top samples
by using a circuit
The sampling process is sometimes referred to as pulse amplitude modulation (PAM).
We need to remember, however, that the result is still an analog signal with Non-integral values.

## Slide 6: What are the restrictions on Ts?
First, a signal with an infinite bandwidth cannot be sampled.
Second, the sampling rate must be at least 2 times the highest frequency, not the bandwidth.

## Slide 8
60 sec/cycle

## Slide 9: Quantization
The result of sampling is a series of pulses with amplitude values between the maximum and minimum amplitudes of the signal.
The set of amplitudes can be infinite with nonintegral values between the two limits.
These values cannot be used in the encoding process.

## Slide 10
The following are the steps in quantization:
  We assume … the original analog signal has … amplitudes between Vmin and Vmax.
  We divide the range into L zones, each of height Δ (delta).
  We assign quantized values of 0 to L − 1 to the midpoint of each zone
  We approximate the value of the sample amplitude to the quantized values

## Slide 11
−20 and +20 V We decide to have eight levels (L = 8). This means that
Δ = 5 V.
20
15
10
5
0
-5
-10
-15
-20

## Slide 12
the first row is the normalized value for each sample
(actual amplitude/ Δ ).
Notes: pulse amplitude modulation (PAM)

## Slide 13: Original Signal Recovery

## Slide 14: Delta Modulation (DM)
Modulator
The modulator is used at the sender site to create a stream of bits from an analog signal.
The process records the small positive or negative changes, called delta δ.
If the delta is positive, the process records a 1;
if it is negative, the process records a 0.

## Slide 15
The modulator, at each sampling interval, compares the value of the analog signal
with the last value of the staircase signal.
If the amplitude of the analog signal is
larger, the next bit in the digital data is 1; otherwise, it is 0.
If the next bit is 1, the staircase maker
moves the last point of the staircase signal δ up; if the next bit is 0, it moves it δ down.
Note that we need a delay unit to hold the staircase function for a period between two comparisons.

## Slide 16: Delta Modulation (DM)

## Slide 17: Transmission Modes

## Slide 19: Asynchronous Transmission
Asynchronous transmission is so named because the timing of a signal is unimportant.
Instead, information is received and translated by agreed upon patterns.

## Slide 20: Synchronous Transmission

## Slide 21: Isochronous
In real-time audio and video, in which uneven delays between frames are not acceptable, synchronous transmission fails.
The isochronous transmission guarantees that the data arrive at a fixed rate.