## Slide 1
Dr. Asif Zaman
Professor, CSE, RU
CSE3251
Computer Networks

## Slide 3
Medium Access Sublayer

## Slide 4: Ethernet
Many of the designs for PAN, LAN, and MAN… standardized under the name of IEEE 802.
A few have survived but many have not.
The most important of the survivors are:
  802.3 (Ethernet) and
  802.11 (wireless LAN)
  Bluetooth (wireless PAN) is widely deployed but has now
  been standardized outside of 802.15.
  With 802.16 (wireless MAN)

## Slide 5
The 802.11 standard, approved in 1997, applies to wireless LANs with a 1 or 2 Mbps transmission rate in the 2.4 GHz band.
Sometimes the term 802.11 is used to refer to the 802.11x family of specifications.
FHSS (Frequency-hopping Spread Spectrum)
DSSS (Direct-sequence Spread Spectrum)
OFDM (Orthogonal Frequency Division Multiple-Access)

## Slide 8
802.11b
In September of 1999,
It supports a maximum bandwidth up to 11Mbps in the 2.4GHz S-Band Industrial, Scientific, and Medical (ISM) frequency range.
Being an unregulated frequency, 802.11b device can suffer from interference from other wireless users, cordless phones, microwave ovens and other devices using the same 2.4 GHz band.

## Slide 9
802.11a
About the same time 802.11b was created, 802.11a was created.
802.11a supports a maximum bandwidth up to 55Mbps in the 5GHz band.
An advantage of 802.11a is that it operates at a radio frequency that's less clogged by competing signals from other wireless users, cordless phones and microwave ovens.
But 802.11a was not popular due to the more expensive cost of 5GHz components and not being compatible with 802.11b.

## Slide 10
802.11g
In June 2003, 802.11g was released to provide maximum bandwidth up to 55Mbps in the 2.4GHz band.
802.11g is backward compatible with 802.11b because they both use the same 2.4GHz radio frequency.
However 802.11g again suffers from the same interference as 802.11b in the crowded 2.4 GHz range, But 802.11g provides better security features, such as WiFi Protected Access (WAP) and WPA2 authentication with pre-shared key or RADIUS server.

## Slide 11
802.11n
In October 2009 the IEEE approved 802.11n wireless communication standard to provide a maximum bandwidth up to 300Mbps. 802.11n can operate in the 2.4GHz or 5GHz band, and is backward compatible with 802.11a (5GHz band), 802.11b (2.4GHz band) and 802.11g (2.4GHz band) devices.
The 802.11n standard supports MIMO (Multiple Input, Multiple Output) antennas. 802.11n operates on both the 2.4 GHz and the 5 GHz bands. Support for 5 GHz bands is optional. It operates at a maximum net data rate from 54 Mbps to 600 Mbps.

## Slide 12
802.11ac
IEEE 802.11ac delivers speeds ranging from 433 Mbps up to several gigabits per second. It works exclusively in the 5GHz band. 802.11ac operates up to eight MIMO (Multiple Input, Multiple Output) antennas. It uses beamforming technology which sends the signal directly to client devices.

## Slide 15: Ethernet
Two kinds of Ethernet exist:
  Classic Ethernet
  Switch Ethernet
Classic Ethernet: ran at rates from 3 to 10 Mbps.
Switched Ethernet: runs at 100, 1000, and 10,000 Mbps, in forms called
  fast Ethernet,
  gigabit Ethernet, and
  10 gigabit Ethernet

## Slide 16: Ethernet
Classic Ethernet:
  Classic Ethernet snaked around the building as a single long cable to which all the computers were attached.

## Slide 17: Ethernet
Classic Ethernet:
  Thick Ethernet
    The first variety, popularly called thick Ethernet, resembled a yellow garden hose, with markings every 2.5 meters to show where to attach computers.
    500m per segment
    100 machine /segment
  Thin Ethernet
    which bent more easily and made connections using industry-standard BNC connectors
    185m per segment
    30 machine / segment

## Slide 18: Ethernet
Each version of Ethernet has a maximum cable length per segment (i.e., unamplified length) over which the signal will propagate.
To allow larger networks, multiple cables can be connected by repeaters.
A repeater is a physical layer device that receives, amplifies (i.e., regenerates), and retransmits signals in both directions.
An Ethernet could contain multiple cable segments and multiple repeaters, but no two transceivers could be more than 2.5 km apart and no path between any two transceivers could traverse more than four repeaters

## Slide 19: Ethernet
Collision Doman
Hub vs Switch
Working procedure of switch

## Slide 20: Ethernet

## Slide 21: Hub vs Switch vs Router